## Slide 1: Microcontrollers
Module 4: Motion Control

## Slide 2: Module Objectives
Upon successful completion of this module, students will be able to:
Give examples of microcontroller motion control applications.
Explain the basics of servo motors and control.
Program the BASIC Stamp Microcontroller to control the angle and speed of the Servo Motor.

## Slide 3: Introduction to Motion Control
Microcontrollers control the motion of many things in our daily lives; a few examples are given below:
Printer head movement
DVD and VCR mechanisms
automatic doors
Robotic movement

## Slide 4: Microcontroller Motion Control Applications

## Slide 5
The examples of motion devices/motors are as follows:
DC Motors
AC Motors
Stepper Motors
Servo Motors
Instead of simple ON/OFF signals, most of these motion devices require very fast pulses of signals for position control or movement

## Slide 6: Servo Motor
The hobby servo or the Servo motor is the simplest and most directly useful of all DC motors
could be controlled from the BASIC Stamp.
A servo motor can be found in many devices that we use every day.
Movement of the print head in an inkjet printer
Automatic eject feature in VCR and DVD players.
Opening and closing of automatic doors in shopping malls, hospitals and so on.

## Slide 7
Unlike other motors,
a servo motor does not
have a continuous shaft
Rotation
can only rotate between two
defined angles.

## Slide 8: Servo Motor Control
Since the control signal of the servo motor is separate from the power signal.
all three wires should be connected as shown in Figure

## Slide 9: Servo Motor Connection
Wire | Connected to | Purpose
White | P14 or any other microcontroller output pin | The control signal from the microcontroller will control the rotation of the motor towards a targeted angle
Red | Vdd or +5V | To supply power to the motor
Black | Vss | Ground connection

## Slide 10
A servo motor is controlled by very short high signalsor pulses spaced 20ms apart as illustrated in figure below.
The duration of a pulse is between 1ms and 2ms.

## Slide 11
The duration of the high signal determines the targeted angle the servo motor should be positioned at.
For example, 1ms high signal duration causes the servo motor (red marked corner) to be positioned at angle zero degree,
1.5ms sets it at 45 degrees and
2ms sets the angle at 90 degrees as shown in figures

## Slide 12
Motor rotation | Signal duration | Targeted angle
 | I ms | 0 degrees
 | 1.5 ms | 45 degrees
 | 2ms | 90 degrees

## Slide 13: Programming the BASIC Stamp for Servo Control
PULSOUT Command:
The PULSOUT command is used to send the signal to control the movement of the servomotor.
The command syntax is as follows:
PULSOUT pin, duration
Pin: defines which I/O pin to use
Duration: defines the duration of a single pulse in microseconds.

## Slide 14
Note :
The PULSOUT duration is in 2microsecond increments.
1 s = 10-6 seconds.
1000s = 1ms s - Microsecond

## Slide 15: Example
The command
PULSOUT 14, 750
would be sending a pulse that lasts
750 x 2 s = 1500 s or 1.5ms on pin 14

## Slide 16
To calculate the duration if the time period is in ms, the following formula could be used:
Duration = Time (ms) X 500
Time (ms) | Duration
1 ms | 500
1.5 ms | 750
2 ms | 1000

## Slide 17
The following program code could be used to generate 150 pulses, each of duration 1000 (or 2ms) with 20ms pauses.

## Slide 18: Timing diagram

## Slide 19: Exercise
1. Write the BASIC Stamp program code to generate 200 pulses, each of duration 1.5ms.
2. Write the BASIC Stamp program code to generate 150 pulses, each of duration 500

## Slide 20: Solution - 1

## Slide 21: DEBUGIN Command
The DEBUGIN command is used to send a value from the debug terminal to the microcontroller,
And the value is stored in the declared variable.
Command Syntax:
    DEBUGIN DEC Variable

## Slide 22: EXAMPLE
In the command
DEBUGIN DEC Pulses
a decimal value will be sent from the debug terminal to be stored in the variable Pulses.
DEC indicates that the value stored is a decimal number.

## Slide 23: COMPARE DEBUG COMMAND AND DEBUGIN COMMAND
DEBUG COMMAND
DEBUGIN COMMAND